Desiccant Recommendation Chart

Unit Bags

- Silica Gel Beaded				  *Calculate the Volume or Area of your container

- Clay						    and choose the type of desiccant desired.

| Volume | Area | Units Required |
| --- | --- | --- |
| Cu Inches | Cu Feet | Gallons | Sq inches | Sq Feet |  |
| 237 | 0.14 | 1.10 | 15 | 0.10 | 1/6 |
| 476 | 0.28 | 2.10 | 30 | 0.20 | 1/3 |
| 715 | 0.42 | 3.20 | 45 | 0.30 | 1/2 |
| 1,429 | 0.83 | 6.20 | 90 | 0.60 | 1 |
| 2,857 | 1.67 | 12.50 | 180 | 1.30 | 2 |
| 4,286 | 2.50 | 18.70 | 270 | 1.90 | 3 |
| 5,714 | 3.33 | 25.00 | 360 | 2.50 | 4 |
| 7,143 | 4.17 | 31.20 | 450 | 3.10 | 5 |
| 8,571 | 5.00 | 37.40 | 540 | 3.80 | 6 |
| 10,000 | 5.83 | 43.60 | 630 | 4.40 | 7 |
| 11,423 | 6.67 | 50.00 | 720 | 5.00 | 8 |
| 12,857 | 7.50 | 56.10 | 810 | 5.60 | 9 |
| 14,286 | 8.33 | 62.30 | 900 | 6.30 | 10 |
| 17,143 | 10.00 | 74.80 | 1,080 | 7.50 | 12 |
| 20,000 | 11.67 | 87.30 | 1,260 | 8.80 | 14 |
| 22,857 | 13.33 | 99.70 | 1,440 | 10.00 | 16 |
| 28,571 | 16.67 | 125.00 | 1,800 | 12.50 | 20 |
| 42,857 | 25.00 | 187.00 | 2,700 | 18.80 | 30 |
| 57,143 | 33.33 | 249.00 | 3,600 | 25.00 | 40 |
| 71,429 | 41.67 |  | 4,500 | 31.30 | 50 |
| 85,714 | 50.00 |  | 5,400 | 37.50 | 60 |
| 100,000 | 58.30 |  | 6,300 | 43.80 | 70 |
| 114,286 | 66.67 |  | 7,200 | 50.00 | 80 |

* A “unit” of desiccant refers to its drying capacity, not its volume. A unit (approx. one ounce)

is the amount of desiccant that will adsorb at least 3 grams of water vapor at 20% relative

humidity and at least 6 grams of water vapor at 40% relative humidity at 77°F (25°C).

Pillow Paks and Continuous Strip Paks

| Container Size Cubic CM | Required Amount (grams) |
| --- | --- |
|  | Silica Gel | Activated Carbon | S.G./Carbon (50/50) |
| 30 | 1/8 | 1/4 | 1/4 |
| 40 | 1/4 | 1/4 | 1/4 |
| 50 | 1/2 | 1/4 | 1/4 |
| 60 | 1/2 | 1/2 | 1/2 |
| 75 | 3/4 | 1/2 | 1/2 |
| 100 | 1 | 1 | 1 |
| 150 | 1 | 1 | 1 |
| 200 | 2 | 2 | 2 |
| 300 | 2 | 2 | 2 |
| 400 | 3 | 2 | 3 |
| 500 | 3 | 2 | 3 |
| 750 | 5 | 2 | 5 |
| 950 | 5 | 5 | 5 |